## Slide 1: Introduction to Basic Manufacturing Process Lab ME29201
Demonstration of measurement of surface roughness generated using turning and end milling
Department of Mechanical Engineering IIT Kharagpur

## Slide 2
Turning operation
Turning is the removal of metal from the outer diameter of a rotating cylindrical workpiece.
Illustration of turning operation [1]
Chip formation during turning operation [2]

## Slide 3
End-milling operation
Milling is the process of machining using rotary cutters to remove material by advancing a cutter into a workpiece.
Illustration of end-milling operation [3]
Machine set-up for end milling
[IIT Kharagpur lab]

## Slide 4
Talysurf Surface Profilometer
Illustration of working model of Talysurf surface roughness tester [4]

## Slide 5
Advantage and limitations of Talysurf Surface Profilometer
Advantages
Its response is more rapid.
It is accurate as compared to Tomlinson Surface meter.
It gives ×20 and ×100 horizontal magnification.
Limitations
Initial cost is high.
Measurements are limited to a section of a surface.
Needs skilled operators for measurements.
Distance between stylus and skid and the shape of the skid introduce errors in measurement for wavy surfaces.
Talysurf surface roughness tester [5]

## Slide 6
Surface Roughness and Waviness
Illustration of surface roughness and waviness in 3D and 2D [6]

## Slide 7
Filter technique of surface roughness from waviness
Filtering surface profile involves running a “smoothing” filter through the primary data.
Shorter wavelengths fall into the roughness profile.
Longer wavelengths appear in the waviness profile.
“Gaussian” filter is recommended in ASME and ISO standards [7]

## Slide 8
Surface roughness parameter (Deterministically)
Important parameters
Rp : Maximum profile peak height
Ry : Maximum height of irregularities
Rv : Maximum profile valley depth
Ra : Arithmetic mean deviation/ arithmetic average
Representation of surface roughness parameter [8]

## Slide 9
Surface roughness parameter (Deterministically)
Rz : Average maximum height of the profile
RMS : Root mean square method (geometrical average)
=

## Slide 10
Surface roughness parameter (Probabilistically)
Mean (Ra) =
RMS (Rq) =
RMS : Root mean square Roughness
Ra : Arithmetic mean deviation or arithmetic average

## Slide 11
References
[1] Tosun, Nihat & Özler, Latif. (2004). Optimisation for hot turning operations with multiple performance characteristics. The International Journal of Advanced Manufacturing Technology.
[2] http://www.mini-lathe.com/Mini_lathe/Operation/Turning/turning.htm
[3] A Study of the Effects of Machining Parameters on the Surface Roughness in the End-Milling Process. Jordan Journal of Mechanical and Industrial Engineering. 1.
[4] https://www.taylor-hobson.com
[5] https://what-when-how.com/metrology/direct-instrument-measurements-metrology/
[6] J.Raja, et al (2002). Recent advances in separation of roughness, waviness and form. Precision
Engineering. 26. 222-235. 10.1016/S0141-6359(02)00103-4.
[7] https://digitalmetrology.com/tutorials/3-steps-to-understanding-surface-texture/
[8] https://roslerblog.com/2016/05/27/surface-roughness-measurement/